## Slide 1: Tx Driver - CML
1 Gbps
Muhammad Aldacher

## Slide 2: Current-Mode Logic (CML)
Higher Vswing means:
Higher SNDR, but Higher Power also

## Slide 3: 1) Without Replica
Vin+
Vin–
Vout+
Vout–
Device Sizing:
Input devices (M1 & M2) act as switches, so we should increase W (reducing RON) to improve headroom.
Bias devices (Mbias & Mmirror) should have large L to reduce channel length modulation. Also we need to increase their W to reduce their VGS & VOV.
M1 = M2 : L = LMIN , m=100x
Mbias = Mmirror : L = 4 * LMIN , m=200x

## Slide 4: 2) With Replica
Vin+
Vin–
Vout+
Vout–
M1 = M2 = Mr1 : L = LMIN , m=100x
Mbias = Mmirror : L = 4 * LMIN , m=200x

## Slide 5: Testbenchs & Setups
VDD = 1V
Data-Rate = 1 Gb/s
VSWING = 0.5V (pk2pk)
IBIAS = 10mA

## Slide 6: Testbench A) Without Replica
VDD=1V
LIB: analogLib
CELL: vprbs
Zero value: 0 V / 1 V
One value: 1 V / 0 V
Bit period: 1 ns
Rise/Fall times: 20 ps
Edge type: linear
Trigger: Internal
LFSR Mode: PN32

## Slide 7: Testbench B) With Replica
VDD=1V

## Slide 8: Channel Settings (mtline)
For Zo = 50 Ohms:
Dielectric_const = = 4.8
Dielectric_thickness = H = 360u
Line_width = W = 625u
Line_thickness = T = 17.78u

## Slide 9: Ideal OpAmp
vcvs
(analoglib)

## Slide 10: Simulation Setup

## Slide 11: Measurements
eyeDiagram(VT("/outp_load")-VT("/outn_load") 0 VAR(“sim_time") 2n ?autoCenter t )
2*UI

## Slide 12: Simulations & Results

## Slide 13: Waveforms
–250 mV
+250 mV
VSWING(PK2PK) = 500 mV

## Slide 14: Waveforms (Eye-Diagrams)
(For more info on how to measure Eye Diagrams)
No Replica:
VSW(pk2pk) = 496.18 mV
With Replica:
VSW(pk2pk) = 499.9 mV
 More Accurate Swing, at the expense of an extra branch + additional power drawn by the OpAmp

## Slide 15: Current Consumption
Total current drawn = 20 mA
(10 mA from main driver + 10 mA from current branch/Replica)